## Slide 1: MT6589 Preloader DRAM code
Internal Use
Copyright © MediaTek Inc. All rights reserved.
2012/12/14

## Slide 2: Files list
File Name | Function
mt_emi.c | mt_set_emi() is the entry point which will call pll init, dram init, and calibration functions.
 | This file includes entry point function, dram initialization.
dramc_calib.c | Include the RX DQ/DQS per bit and TX DQ/DQS per byte calibration.
dramc_dle_cal.c | Include the DLE calibration code
dramc_dqs_gw.c | Include the DQS gating window calibration code.
mtk_pll.c | Include the code for mempll init and calibration code.
custom_emi.c | Used to keep the customization settings for different memory part. But now is not using.

## Slide 3: Structure
cbs (callback structure)
  Main usage
    Before entering recursive call, need to setup the structure with customized routines.
  Member functions
    ett_print_banner(n)
      Will be called in the beginning of every recursive call. In general, it will be used to print the header in case of n==1.
    ett_print_before_start_loop_zero
      Will be called only in the most inner loop (n=0) (before starting loop 0)
    ett_print_before_each_round_of_loop_zero
      Will be called only in the most inner loop (n=0) (before each round of loop 0)
    ett_print_result
      Will be called only in the most inner loop (n=0)
      Main routine which is doing the calibration test in loop 0.

## Slide 4: Structure
cbs (callback structure) (cont’)
  Member functions (cont’)
    ett_print_after_each_round_of_loop_zero
      Will be called only in the most inner loop (n=0) (after each round of loop 0)
    ett_calc_opt_value (n, &score, &high_score) :
      Will be called for every loop.
      In general, it is used for n=1 to choose the optimized settings. score will be accumulated for the return value of ett_print_result. High_score is used to record the highest score and compared with score.
    ett_print_after_finish_loop_n(n)
      Will be called for every loop. In general, it is used for print '\n' before leaving a loop for example.

## Slide 5: Structure
test_case
  Main usage
    It is used in cbs.ett_print_result() for customized calibration testing.
  Member functions
    test_case()
      routine to do the test with starting address, range, and ext_arg.
    start : starting address.
    range : testing range.
    ext_arg : external argument.

## Slide 6: Structure
tuning_factors
  Main usage
    define the dimension of calibrations and the corresponding parameters' settings and method.
  Member functions
    name : name of calibration items.
    factor_table[] : array of different calibration values.
    curr_val : current setting value.
    opt_val : optimized setting value.
    factor_handler() : method to set the parameter.

## Slide 7
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com